## Slide 1: Computational X-Ray Fluorescence (XRF) Imaging using Dictionary Learning
Qiqin Dai1, Emeline Pouyet2, Oliver Cossairt1,
Marc Walton2, Aggelos Katsaggelos1,
Francesca Casasdio2
1Northwestern University, 2NU-ACCESS
Notes: Good Morning/Hello. I am Ollie Cossairt, director of the NU comp imaging lab where we work on a variety of projects related to imaging, photography, image processing, computer vision and graphics. Today I will talk about Imaging Technologies for Surface Shape Study of the Art of Paul Gauguin. This is work that was done as part of a large collaboration between the NU Comp Photo Lab, the AIC, NU-ACCESS, the Georgia O-Keefe Museum, Scripps College, and ANE Imaging.

## Slide 2
Ultraviolet (280-400 nm)
Visible (450-750 nm)
Infrared (750-2000nm)
X-ray (sub 10 nm)
Why Imaging of Art? Different modalities to interrogate structure
Notes: The size of a pigment particle varies considerably from less than 10 micrometers, which is comparable to milled flour to over 100 micrometers, which corresponds to fine sand.

## Slide 3
X-Ray Radiography & X-Ray Fluorescence Imaging
Röntgen, X-Ray Shadowgraph, 1890’s
Notes: Ana Bertha Ludwigs hand

## Slide 4: Early History of Imaging of Artworks: X-Ray
Alan Burroughs, Fogg Museum, Harvard, 1938
A. Burroughs, Art Criticism from the Laboratory, 1938
Notes: Alan Burroughs Art Criticism from the Laboratory, 1938
Harvard University's Fogg Museum on the development of a scientific approach to conservation. Edward Forbes (1873-1979), who became director of the Fogg in 1909, was the driving force behind this initiative. When he began collecting Renaissance and medieval paintings in poor condition, he became interested in the artists’ materials and how the chemical makeup of works related to their degradation over time. Among his collaborators at the Fogg were Alan Burroughs, the first art historian to use x-rays to examine paintings, and Rutherford Gettens, the first chemist to work in an art museum’s scientific laboratory.

## Slide 5: X-Ray Fluorescence (XRF) Imaging
Cu Ka, Kb
Energy (KeV)
Intensity (log scale)
SD Detector
Rh tube with 1mm spot
camera
10 cm x 10 cm scan stage
Cu Ka Map

## Slide 6
Characterizing Unique Artworks Necessitates Non-Invasive Techniques
X-Rays
XRF
detector
Fluorescence energy
Counts number
Elemental Analysis
Fe
Cu
Zn
Cr
Pb
Handled X-Ray Fluorescence Spectrometer

## Slide 7: XRF maps let you see the invisible!
Beam size –Step size 200x200µm²
Dwell time 10ms/point - Att (6)
Fe K- line
Hesiod Manuscript (RGB Image)
XRF Map (Iron)

## Slide 8
Pb Ka
Hg Ka
Fe Ka
Cu Ka
XRF Re-colorization of Hidden Layers
Rembrandt, An Old Man in Military Costume (1630), J. Paul Getty Museum, 78.PB.246
Trentelman, Karen, et al. "Rembrandt’s An Old Man in Military Costume: the underlying image re-examined." Applied Physics A 121.3 (2015): 801-811.

## Slide 9: XRF Scanner Advantages & Disadvantages
Advantages
  Deep X-Ray penetration into hidden layers
  Elemental composition for chemical characterization and provenance analysis
  High spectral resolution (4096 channels)
Disadvantages
  Low Signal-to-Noise-Ratio (SNR)
  Slow raster scan process -> Low spatial resolution
  A typical XRF scan takes 2sec/pixel -> 20,000 s (6hr) for a 100x100 XRF map)

## Slide 10: How can we make scanning Faster?
Carbon
Iron
Lead
…
Mercury
Captured XRF Datacube
Elemental XRF Dictionary
  Observation: The XRF Spectra span a small subspace in
  Approach: Use dictionary methods to model XRF spectra using a linear basis decomposition

## Slide 11: How can we make XRF scanning faster?
Denoising -> Shorter exposure times for each pixel
Express each pixel spectra in a dictionary basis
Super-resolution -> Faster raster scanning
Enforce a spatial prior to increase resolution
Spatial
Prior
RGB Image Fusion -> Faster raster scanning
Incorporate HR RGB image and coupled RGB-XRF spectral dictionary
RGB
Dictionary
RGB
Image

## Slide 12
Vincent Van Gogh, The Bedroom (1889)
Art Institute of Chicago 1926.417

## Slide 13
XRF Scanning of Van Gogh’s Bedroom
Notes: Vincent van Gogh Dutch, 1853-1890
Eosin Y is an early synthetic dye that was utilized among nineteenth century artists. The potassium or sodium salt of 2,4,5,7-tetrabromofluorescein was first made in 1871 and used for making inks. As a lake pigment, it makes a brilliant bluish red and was sold under the name of geranium lake. Van Gogh used the dye quite extensively, but unfortunately it has almost invariably faded in many of his paintings
13

## Slide 14: Denoising using XRF Dictionaries
Captured XRF Cube
XRF Dictionary
Denoising:
Denoised XRF Cube
Input
Output

## Slide 15: Denoising results
Denoised XRF Cube
Captured (Noisy) XRF Cube

## Slide 16: Denoising results
Denoised XRF Cube
95x95Pixels
(Cobalt, Channel 857)
Area scanned using MA-XRF
38x38cm²
Step size: 0.400 cm
38cm
38cm
Captured XRF Cube
95x95Pixels
(Cobalt, Channel 857)
Cobalt distribution - from Cobalt Blue pigment CoAl2O3

## Slide 17: Superresolution using XRF Dictionaries
Captured XRF Cube
XRF Dictionary
High Res XRF Cube
Input
Output
Superresolution:
Spatial
Prior
Superresolution
CNN

## Slide 18: Superresolution using XRF Dictionaries
[Dong et al., ECCV 2014]
Regularized Dictionary Learning:
Spatial Superresolution:
XRF Cube Reconstruction:
Denoising
Objective
Spatial smoothness
for neighbor pixels
Positivity
Constraints

## Slide 19
95x95Pixels
190x190Pixels
Area scanned using MA-XRF
38x38cm²
Step size: 0.400 cm
38cm
38cm
Superresolution Results
Denoised XRF Cube
Captured XRF Cube
Cobalt distribution - from Cobalt Blue pigment CoAl2O3
Using Region of Interest over XRF Spectrum

## Slide 20: Superresolution Results
Baseline #1: Super resolve each channel of the captured XRF cube independently using SCNN
Baseline #2: Denoise captured XRF cube then Super resolve each channel of the captured XRF cube independently using SCNN
  Our superresolution technique gives the best visual quality and fastest computation time for the Bedroom dataset

## Slide 21: XRF Super-Resolution + RGB Image Fusion
Conventional
RGB image
Super-resolution
HR XRF image
XRF Scanner
Conventional Camera
Super-resolution + Fusion algorithm
Vincent Van Gogh, The Bedroom (1889)
Art Institute of Chicago 1926.417
Captured XRF Cube

## Slide 22: RGB Fusion using XRF Dictionaries
XRF Cube
Input
XRF Dictionary
High Res XRF Cube
Output
RGB Dictionary
HR RGB Image
Superresolution + Fusion:
Coupled Sparse Coefficients
Downsamping
Matrix

## Slide 23
95x95 Pixels
475x475 Pixels
Area scanned using MA-XRF
38x38cm²
Step size: 0.400 cm
38cm
38cm
Fusion Results
Fused XRF Cube
Captured XRF Cube
CrK Peak, Bands 611-657

## Slide 24
Superresolution (475x475 pix)
RGB Fusion (475x475pix)
Input (95x95 pix)
Mercury (Bands 1078-1105)
Arsenic (Bands 1243-1290)

## Slide 25
Superresolution (475x475 pix)
RGB Fusion (475x475pix)
Input (95x95 pix)
Mercury (Bands 1078-1105)
Arsenic (Bands 1243-1290)

## Slide 26
Superresolution (475x475 pix)
RGB Fusion (475x475pix)
Input (95x95 pix)
Cobalt (Bands 840-875)
Copper (Bands 875-892)

## Slide 27
Superresolution (475x475 pix)
RGB Fusion (475x475pix)
Input (95x95 pix)
Cobalt (Bands 840-875)
Copper (Bands 875-892)

## Slide 28: What about hidden layers?
XRF Cube
High Res XRF Cube
Input
Output
HR RGB Image
Visible
XRF Cube
High Res XRF Cube
Not Visible
High Res XRF Cube

## Slide 29: RGB Fusion Model for Hidden Layers
: Low resolution input XRF image
: Visible part of
: Non-visible part of
Input high resolution RGB image
: Spatial down-sample matrix
Inputs
Superresolution + Fusion + V/NV:
Reconstruction:
Non- Visible
Visible
Visible
Coupled Coefficients
Non-Visible
Total Variation
Superresolution
: XRF dictionary (visible)
: XRF dictionary (non-visible)
: RGB dictionary
: Coefficient of visible component
: Coefficient of non-visible component
Outputs

## Slide 30: Hidden Layer Optimization Algorithm

## Slide 31: Hidden Layer Example
Layer 1
Layer 2
(hidden)
XRF Spectra
XRF Cube
RGB Image

## Slide 32: Hidden Layer Example
LR Input
HR Ground Truth
Proposed Method
No Hidden Layer Model

## Slide 33: Conclusions and Future Work
XRF mapping is an emerging method for cultural heritage research
RGB Fusion methods can reduce scan time by 4x-20x
Hidden layer modeling still under development
Need more ground truth HR XRF measurements for quantitative comparisons
Want to explore different sampling strategies